## Slide 1
AI-Based Fire Fighting Robot using ESP32
An autonomous, IoT-enabled robot designed to detect, navigate, and extinguish fires — with real-time WhatsApp alerts
Team
Arun Kumar · Priya S · Karthik R · Divya M
Department
Electronics & Communication Engineering
Institution
Anna University, Chennai

## Slide 2
Introduction
The Problem
Fire accidents cause thousands of casualties and billions in property damage annually. Traditional firefighting relies heavily on manual intervention — placing human lives at serious risk in unpredictable, high-heat environments.
Delayed response time in large buildings
Firefighters exposed to toxic fumes and extreme heat
Manual systems lack real-time monitoring
The Solution
Autonomous fire-fighting robots bridge this gap by combining embedded systems, sensor fusion, and IoT connectivity to detect and respond to fires faster — without putting humans at risk.
Automation is no longer optional in fire safety — it is a necessity.

## Slide 3
Project Objectives
Four core goals drive this project, from sensing to action to communication.
Detect Fire Automatically
Use three flame sensors to triangulate fire position with high accuracy in real time.
Navigate Towards Fire
Drive DC motors intelligently to steer the robot in the direction of the detected flame.
Extinguish the Fire
Activate the water pump and servo motor to spray water precisely at the fire source.
Send Real-Time Alert
Trigger a WhatsApp notification via WiFi API the moment fire is detected.

## Slide 4
System Overview
The robot follows a closed-loop sense → decide → act → communicate pipeline.
WiFi Alert
Water Pump
Motor Driver
ESP32 Processing
Flame Sensors
The ESP32 microcontroller acts as the brain — reading sensor data, controlling actuators, and managing wireless communication simultaneously through its dual-core architecture.

## Slide 5
Components Used
Microcontroller
ESP32 DevKit V1 — dual-core, built-in WiFi & Bluetooth
Sensing
3× Flame Sensors (analog IR-based, 60° detection angle each)
Actuation
TT DC Motors + L298N Driver · SG90 Servo · 5V Water Pump + Relay
Power
18650 Li-ion Batteries + LM2596 Buck Converter for regulated supply

## Slide 6
Block Diagram
Signal Flow Summary
Sensors → ESP32: Analog flame intensity values read on GPIO pins
ESP32 → L298N: PWM signals control motor speed and direction
ESP32 → Servo: PWM positions nozzle at fire source
ESP32 → Relay: Digital HIGH triggers the water pump
ESP32 → WiFi: HTTP GET request to CallMeBot WhatsApp API
All control logic runs on ESP32's core 0 while WiFi communication uses core 1 for non-blocking operation.

## Slide 7
Working Principle
1
Flame Detection
Left, centre, and right sensors output analog values. Lower value = stronger flame signal in that direction.
2
Direction Logic
ESP32 compares sensor readings. Steers left, right, or straight based on which sensor registers the minimum value.
3
Fire Suppression
When centre sensor crosses the fire threshold, the relay activates the pump and servo sweeps to spread water.
4
Alert Dispatch
Simultaneously, ESP32 sends an HTTP request to the WhatsApp API — notifying the operator instantly over WiFi.
The robot continuously loops through this pipeline — stopping all actuators once all three sensors read above the safe threshold, confirming fire extinction.

## Slide 8
Algorithm / Flowchart
Activate Response
Move, pump, alert
Fire Detected?
Threshold comparison
Read Flame Sensors
analogRead on GPIOs
Start
Initialize sensors and loop
Code Structure Highlights
01
Sensor Reading
analogRead() on GPIO 34, 35, 32 — sampled every 100 ms loop cycle
02
Motor Control
digitalWrite() on IN1–IN4 pins of L298N; PWM via ledcWrite() for speed
03
Fire Logic
Threshold comparison (sensorVal < FIRE_THRESHOLD) triggers action
04
WhatsApp Alert
HTTPClient sends GET request to CallMeBot API with encoded message

## Slide 9
Results
<2s
Detection Time
Flame detected and response initiated within 2 seconds of exposure
~1m
Effective Range
Flame sensor reliably detects fire up to 1 metre in open conditions
360°
Servo Sweep
Servo rotates nozzle across full arc for maximum water coverage
5s
Alert Latency
WhatsApp notification delivered within 5 seconds on a stable network

## Slide 10
Advantages, Limitations & Future Scope
Advantages & Applications
Human Safety
Eliminates need for manual intervention in dangerous environments
Wide Applications
Homes, warehouses, industrial plants, small-scale forest monitoring
Low Cost
Built under ₹3,000 using off-the-shelf components
Limitations
Limited water tank capacity — suitable for small fires only
Battery life restricts continuous operation time
Performance degrades in complex terrain or poor WiFi coverage
Future Scope
Integrate ESP32-CAM for real-time visual feedback
Add ML-based fire classification for improved accuracy
Replace WiFi with GSM (SIM800L) for network-independent alerts
Multi-robot coordination for large-scale environments